## Slide 1: Final Evaluation – AT Command SMS Flow Summary

## Slide 2: OBJECTIVE
Simulate a real-world SMS interaction using a GSM AT Command sequence via the CelerSMS AT Emulator.

## Slide 3: COMMANDS EXECUTED
• AT – Test modem response → OK
• AT+CSQ – Get RSSI (signal strength) → +CSQ: 21,0
• AT+CMGF=1 – Set SMS format to text mode → OK
• AT+CMGS="+91..." – Send SMS (CTRL+Z to finish) → +CMGS: 1 OK
• AT+CMGR=1 – Read received SMS → OK,

## Slide 4: SETBACKS
Emulator returns ERROR on AT+CMGR=<MSG_ID>.
This is a setback of using emulator instead of real modem, there is nothing to read since no actual message is actually being send

## Slide 5: INFERENCES
• Full flow of AT commands for GSM SMS communication.
• CTRL+Z is required after message for AT+CMGS.
• Emulator limitations vs real GSM module behavior.