## Slide 1: TCP Communication with Cavli Modules using AT Commands

## Slide 2: Explanation of Key Commands
AT+QIOPEN - Opens a TCP/UDP socket connection. - Syntax: AT+QIOPEN=1,0,"TCP","<server>",<port>,0,1
- Returns OK and +QIOPEN: 0,0 (success)
AT+QISEND - Sends data over opened socket. - Syntax: AT+QISEND=0,<length> - Wait for > then type data and press Ctrl+Z - Returns SEND OK

## Slide 3: TCP Communication Flow
Step 1: Set PDP context AT+CGDCONT=1,"IP","<APN>" Step 2: Activate context AT+QIACT=1 Step 3: Open TCP socket AT+QIOPEN=1,0,"TCP","<server>",<port>,0,1 → OK → +QIOPEN: 0,0 Step 4: Send data AT+QISEND=0,<length> → > type data → Ctrl+Z → SEND OK Step 5: Close socket AT+QICLOSE=0